SB52 Wi-Fi BT User Manual

1. How to Get Started with Android Debug Bridge

1.1 Install ADB on Windows: Download the Platform Tools for Windows.

1.2 Extract the zip file after download. You may find it useful to save it in your “C:” drive or Home folder to make it easy to find.

1.3 The SB52 connects to the PC.

1.4 Type “adb devices” in the command window and hit Enter.

cd\

cd platform-tools_r33.0.0-windows

cd platform-tools

adb devices

If it lists your device, you have successfully made the connection.

2. Wi-Fi Test Example

2.1 Enter Test mode and Tx test.

adb root

adb shell

wifitest -O

wifitest -t 1 -c 1 -N 7 -B 0 -s 1 -g 0 -i 30 -S 10 -n 0 -p 17 -y 1 -Y 0

(TX Channel 1, bandwidth 20, MCS7, TX0, 11n, Long Preamble, Packet unlimit, 10 seconds, power 17 dBm)

2.2 Wi-Fi Test Commands List:

Reference attachment 7668-WIFI Command to Wi-Fi test.

3. Bluetooth Test

3.1 BT TX Test Example

boots -c rft -p 1 -c 0 -t 4      //Pattern:0000 Channel:0 Packet type: Null

boots -c rft -p 1 -c 39 -t 4     //Pattern:0000 Channel:39 Packet type: Null

boots -c rft -p 1 -c 78 -t 4     //Pattern:0000 Channel:78 Packet type: Null

3.2 BT RX Test Example

boots -c rft -p 1 -c 0 -t 4 -a xx:xx:xx:xx  //Pattern:0000 Channel:0 Packet type:DH1

boots -c rft -p 1 -c 39 -t 4 -a xx:xx:xx:xx //Pattern:0000 Channel:39 Packet type:DH1

boots -c rft -p 1 -c 78 -t 4 -a xx:xx:xx:xx //Pattern:0000 Channel:78 Packet type:DH1

3.3 BT Stop Command

boots stop

CTRL+C

3.4 BLE TX Test Example

boots -c ble_tx -c 0 -p 1     //Pattern:11110000 Channel:0

boots -c ble_tx -c 19 -p 1    //Pattern:11110000 Channel:19

boots -c ble_tx -c 39 -p 1    //Pattern:11110000 Channel:39

3.5 BLE RX Test Example

boots -c ble_rx -c 0      //Channel:0

boots -c ble_rx -c 19     //Channel:19

boots -c ble_rx -c 39     //Channel:39

3.6 BLE Stop Command

boots stop

CTRL+C

3.7 BT/BLE TX Modulation tone Example

boots -c txtone -t 4 -c 0 -m 0 -d 0 -p 1     //BT Channel:0 1M PRBS15

boots -c txtone -t 4 -c 0 -m 1 -d 0 -p 1     //BLE Channel:0 1M PRBS15

# Text boxes

SB52 I/O Boand

ANT2

WiFi/BT

ANT1

WiFi

12V Adapter

ADB USB Port to PC

SB52 SOM Boand